## Slide 1
A Multi-protocol Fail-Safe Bootloader Framework for Remote Firmware Updates in Automatic Train Protection Systems
Abhinav Pathak, Manu Pratap Shekhawat, Munish Khanna
Central Research Laboratory, BEL Ghaziabad
Notes: Good morning. I'm Abhinav from CRL Ghaziabad. Today I'll show how we update firmware on every card of a Kavach ATP unit from one Ethernet port, and why a failed update never leaves a card dead.

## Slide 2
Content
Agenda
1
Introduction
2
Design Constraints
3
System Architecture
4
How an Image Travels
5
One Updater, Three Links
6
The Links in Detail
7
Block Size Division
8
Transfer Stages
9
Bitmap Selective Repeat
10
Dual-Bank Flash & Memory Map
11
Power-Safe Commit
12
Boot Watchdog & Rollback
13
Image Authentication
14
Timing & Benchmarks
Notes: Here's the plan. We start with the problem, walk through the transfer protocol, then the flash side: dual banks, safe writes, rollback. We close with security and on-target numbers.

## Slide 3
Introduction
ATP is a distributed system
Each onboard and wayside unit has a master controller plus input, output and analog cards.
Manual updates don't scale
Technicians must reach every card on a large fleet. It takes time, and mistakes creep in.
Safety comes first
A failed or corrupted update must never leave a card unable to boot.
What we built
A bootloader that runs on every card, before the application, at every reset.
1
One reliable-transfer protocol for UDP, CAN-FD and UART
2
A coverage bitmap that decides when an image is complete
3
A dual-bank commit that rolls back on its own
Notes: An ATP unit isn't one controller. It's a master plus several I/O cards. Updating each card by hand is slow and risky. We wanted one entry point that reaches every card and can survive anything that goes wrong mid-update.

## Slide 4
Design Constraints
Mixed links
Ethernet brings images in.
CAN-FD and UART carry them to the cards.
Usable payload differs by about 25×.
Separate protocols per link would multiply code and testing.
Unreliable channel
UDP gives no delivery guarantee.
Counting bytes fails in two ways:
Loss: the count never reaches the target, so the transfer stalls.
Duplicates: the count fills up early, so a broken image looks complete.
Never brick
Power can fail mid-write.
Nobody can reach the card to re-flash it.
The card must detect the failure and recover on its own, within a fixed time.
Safety rule (EN 50128 / EN 50129): check every update end to end. If anything fails, fall back to a safe state: the last validated image.
Notes: Three things make this harder than a phone update. The links are different, the channel loses and repeats packets, and the card must never brick. Our design answers each one.

## Slide 5
System Architecture
Host Update Tool (PC)
UDP / Ethernet
all images
Master Controller (VCC)
Verifies every image
Routes by target id in META
Own image → flash locally
Other image → forward to card
Own dual-bank A/B flash
CAN-FD
UART
(fallback)
peripheral controllers
Input Card
Verifies and flashes locally · own dual-bank A/B
Output Card
Verifies and flashes locally · own dual-bank A/B
Analog Card
Verifies and flashes locally · own dual-bank A/B
Every node, master included, runs the same poll-and-repair protocol and commits to its own flash. Only the framing changes from link to link.
Notes: All images enter through the master over Ethernet. The master reads the target id. If the image is its own, it flashes it. If not, it forwards it on the internal CAN-FD bus, and falls back to UART if CAN-FD is down. Every card commits to its own flash and rolls back on its own.

## Slide 6
How an Image Travels
1
Announce
Host sends META: target id, size, CRC-32 and signature.
2
Stream
Host sends DATA blocks. Master checks each block's CRC-32.
3
Verify
Master checks the whole-image CRC-32, SHA-256 and signature.
4
Route
Master reads the target id. Its own image stays. Others go to their card over CAN-FD or UART.
5
Commit
Target copies it to its spare flash bank, then boots the image.
Update-pending boot window: stopping a race
Normal
5 s idle
boots the app
Announced
60 s pending window
waits for the image
A peripheral boots its app after 5 s of silence. The master may still be busy with the image.
So the master announces "update incoming" as soon as it reads the target id, and repeats it.
The card widens its window to 60 s. The limit is fixed, so a bad announce can only delay boot.
Notes: Walk the image left to right. The host sends metadata, then the blocks. The master checks each block, then the whole image. It routes the image by target id. The target commits it: copies it to its spare bank and reboots to try it. The bottom half solves a race: the peripheral would otherwise boot away before the master finishes.

## Slide 7
One Updater, Three Links
Protocol-agnostic updater core
Transfer state machine
Coverage bitmap
CRC-32 + signature check
Dual-bank commit & rollback
Common messages: META · DATA · POLL · STATUS
UDP / Ethernet
lwIP stack
CAN-FD
4 B link assembly
UART
own framing layer
transport adapters
The core is protocol-agnostic.
It handles loss and duplicates the same way on every link.
Each link adds only its framing.
Swap the adapter, keep everything above it.
Every node runs identical code.
Master and peripherals share one receiver.
Less code, less to verify.
That matters most in the update path.
Notes: This is the key design choice. The reliability logic lives in one protocol-agnostic core. It never needs to know which link a block came over. Each link only supplies framing. The master and every peripheral run the same receive code, so we verify it once.

## Slide 8
The Links in Detail
UDP / Ethernet
CAN-FD
UART
Role
External ingress: host → master
Internal fan-out: master → cards
Automatic fallback if CAN-FD fails
Frame
1518 B Ethernet frame
64 B data frame
Byte stream, no native frames
Usable payload
≤ 1472 B after IP/UDP
60 B after 4 B link assembly
We add a framing layer
Block size B
1450 B
47 B
47 B (matches CAN-FD)
Native delivery
Unordered, lossy
Prioritised, lossy
In-order; treated as lossy
Built-in check
UDP checksum
CRC
Parity
In our updater
lwIP stack on the master
Dedicated bus; master is sender
Half-duplex line, 115200 baud
Notes: Here's how each link behaves and what job it does. UDP brings images in fast. CAN-FD fans them out inside the unit. UART is the safety net when the CAN bus is down.

## Slide 9
Block Size Division
UDP / Ethernet: 1500 B MTU
IP 20
UDP 8
Hdr 13
Block B = 1450 B
9 spare
CAN-FD: 64 B frame
Link 4
Header 13
Block B = 47 B
Segments not to scale.
UART has no frame limit.
Long frames corrupt more easily, though. We keep B = 47 so UART and CAN-FD share one layout.
Sizing rule
N = ⌈ image size / B ⌉ bitmap = ⌈ N / 8 ⌉ bytes
For an 800 KB image
565
blocks on UDP
71 B
UDP bitmap
17,430
blocks on CAN-FD / UART
2,179 B
CAN-FD / UART bitmap
Notes: We split the image into N blocks sized to fit one frame. On UDP, 1450 bytes fits the 1500 byte MTU with a little room to spare. On CAN-FD, the 64 byte frame leaves 47 bytes. UART keeps 47 for uniformity. Block count drives bitmap size.

## Slide 10
Four Messages, Every Link
META
42 B · sender → receiver
type
target id
image size
image CRC-32
digital signature
DATA
13 B + ≤ B · sender → receiver
type
offset
length
block CRC-32
payload (≤ B bytes)
POLL
5 B · sender → receiver
type
session CRC-32
STATUS
16 B + bitmap · receiver → sender
type
outcome
session CRC-32
total blocks
received
bitmap len
bitmap*
Session id = whole-image CRC-32 from META.
POLL and STATUS both carry it, so a leftover message from an aborted session can't touch the current one. *Bitmap is sent only when the outcome is INCOMPLETE.
Notes: Only four messages cross the wire, on every link. Each starts with a one-byte type. The whole-image CRC acts as a session id, so a stale poll or status from an aborted session can't corrupt the current one.

## Slide 11
Stages of Transfer
Sender
Receiver
META (×3 on UDP, ×4 on CAN-FD/UART)
META (repeat)
DATA block 0
DATA block 1
✕ lost
DATA block 2 … N−1
POLL
STATUS: INCOMPLETE + bitmap
DATA: only the missing blocks
POLL
STATUS: COMPLETE (×3)
then commit & reboot
1 Announce
The sender repeats META. The receiver resets its buffer, computes N and stores the expected CRC and signature.
2 Bulk send
Every block goes out once. The receiver checks each CRC, stores the block and sets its bit.
3 Poll / repair
The receiver answers each poll. The sender resends only the missing blocks, then polls again.
STATUS outcomes
COMPLETE
INCOMPLETE
NEED_META
IMAGE_FAIL
Stops on COMPLETE, or when the round or poll-retry budget runs out.
Notes: Three phases. Announce: the sender repeats META so one lost copy can't kill the session. Bulk send: every block goes out once. Poll and repair: the receiver says what's missing, the sender resends only that. The receiver replies COMPLETE before it commits and reboots, and repeats that reply three times.

## Slide 12
Bitmap Selective-Repeat Retransmission
After bulk send
0
1
1
1
2
1
3
0
lost
4
1
5
1
6
1
7
0
CRC ✕
8
1
9
1
10
1
11
1
12
0
lost
13
1
14
1
15
1
bitmap
STATUS: INCOMPLETE + bitmap → sender resends only blocks 3, 7 and 12
After repair
0
1
1
1
2
1
3
1
4
1
5
1
6
1
7
1
8
1
9
1
10
1
11
1
12
1
13
1
14
1
15
1
✓ all set
Every channel fault becomes one question: is the bit set?
Lost block
Bit stays clear. The next poll asks for it.
Corrupted block
Block CRC-32 fails. We treat it as lost.
Duplicated block
Lands in the same slot. Coverage doesn't grow.
Reordered block
Addressed by offset. Order doesn't matter.
A repair round is cheap: a 5 B poll plus a reply of at most 87 B for an 800 KB image on UDP.
Notes: Instead of counting bytes, the receiver keeps one bit per block. A good block sets its bit. Anything else leaves it clear. One status message tells the sender exactly which blocks to resend. Every channel fault collapses into the same thing: a clear bit.

## Slide 13
Dual-Bank Flash & Memory Map
QSPI NOR flash, 8 MB
Bootloader / updater
~250 KB code · never self-modified
0x000000
Bank A
1 MB image slot
0x200000
Bank B
1 MB image slot
0x300000
Free
0x400000
Metadata · primary
0x600000
Metadata · backup
0x610000
Free
0x7FFFFF
Not to scale
How the two banks work
One bank is active and runs the application.
Every new image goes to the inactive bank.
The running image is never overwritten, so rollback always has a target.
A new image with the same CRC as the current one is dropped as a duplicate.
What the metadata record holds
Magic 0xA55AB00B
rejects erased (0xFF) or zeroed flash
Active bank
A or B
Per bank
offset, size, image CRC-32
Confirmed flag
set by the app once it works
Boot-attempt count
trial boots without confirmation
Record CRC
detects a torn metadata write
Notes: The 8 MB QSPI flash holds the bootloader, two 1 MB image banks and two copies of the metadata. We always write to the bank that isn't running. The old image stays untouched until the new one proves itself.

## Slide 14
Power-Interruption-Safe Commit
Write image
to the inactive bank
Verify
bank CRC-32
Write backup
metadata copy
Write primary
metadata copy
Reboot
into trial boot
What if power fails here?
During image write or verify
Metadata still points at the old bank. The old image boots.
During backup metadata write
Primary copy is intact and still old. The old image boots.
During primary metadata write
Primary fails its record CRC. We read the backup and start the trial boot.
After both copies are written
Normal trial boot of the new image.
Two of everything
Bank A
image slot
Bank B
image slot
Primary
metadata
Backup
metadata
At every instant, at least one image and one metadata copy are valid.
Notes: We order the writes so that a power cut at any step leaves one good path to boot. Two image slots and two metadata copies give us that. The backup metadata is always written before the primary.

## Slide 15
Boot-Attempt Watchdog & Rollback
Reset
Active bank CRC OK?
yes
Confirmed?
no
Attempts < 3?
no
no
Boot the other bank
yes
Boot the app. No flash write.
yes
Count one attempt, then trial boot
Roll back to the other bank
App confirms itself
The new app marks itself confirmed once it runs correctly.
Three strikes, then rollback
Each reset before that uses one attempt. After 3, we switch banks.
One bank is always confirmed
The first image is confirmed by default, so rollback always has a safe target.
Idle watchdog
No traffic for 5 s: boot the app. 60 s after an update is announced.
Notes: CRC only catches corrupted flash. It can't catch a clean image that crashes. So the bootloader counts trial boots. The new app must confirm itself once it runs correctly. If it resets three times first, we roll back to the other bank. One bank is always confirmed, because the first image is confirmed by default. In steady state the bootloader writes nothing to flash.

## Slide 16
Image Authentication
Host (PC)
Hash the image
SHA-256 over the whole firmware image.
Sign with private key
Signs the digest. The private key never leaves the host.
Send in META
Signature and public key travel ahead of the image.
Controller
Check public key
Hash the received key. Match it with the key hash stored in OTP.
Verify signature
Use the checked key to recover the host's digest.
Hash image & compare
Compute SHA-256 of the image. Match → commit. Else IMAGE_FAIL.
Only signed images run.
An unknown host can't produce a valid signature.
A fake key is rejected.
Its hash won't match the one burned into OTP.
Checks run once, at completion.
Whole-image CRC-32 first, then the signature.
Notes: CRC protects against accidents, not attackers. So the host signs the image. The host hashes the image with SHA-256 and signs that digest with its private key. The host sends its public key along with the signature. The controller first hashes that key and matches it with the key hash stored in OTP, so a fake key is rejected. Then it uses the key to verify the signature, recomputes the image hash and compares. Only a match gets committed. This part is designed and integration is in progress.

## Slide 17
Timing & Benchmarks
Chart: Transfer time for an 800 KB image (seconds)
| UART | CAN-FD | UDP
Transfer time (s) | 105.9 | 4.1 | 0.92
UDP
CAN-FD
UART*
Throughput
7.1 Mbps
1.6 Mbps
0.1 Mbps
Repair rounds
4
1
2
Repair round time
0.08 s
0.1 s
1 s
Mean of 10 runs, 800 KB image, nominal conditions. *UART at 115200 baud.
Resource footprint
250 KB
bootloader flash
1.5 MB
bootloader RAM
800 KB
staging buffer (master)
160 KB
CAN / UART matrix (cards)
~2 KB
retransmission bitmap
Notes: We measured end-to-end time from the first META to the first COMPLETE. Ten runs, 800 KB image, nominal conditions. UDP moves the image in under a second, CAN-FD in about four. UART is slow but it's a fallback, and it still finishes in under two minutes. Repair rounds stay cheap on every link.

## Slide 18
Conclusion & Future Scope
What we showed
One reliable-transfer protocol serves UDP, CAN-FD and UART.
A coverage bitmap tells the sender exactly which blocks to resend.
The receiver reports COMPLETE before it reboots, so the host always knows.
Dual banks with backup-first metadata survive a power cut at any step.
A boot-attempt watchdog rolls a bad image back on its own.
Every controller runs all of this independently.
Future work
A self-updating controller network
1
Controllers discover each other automatically.
2
They compare firmware versions across the network.
3
Updates spread node to node, without central control.
Notes: To sum up: one protocol over three links, a bitmap that makes loss and duplication harmless, and a flash commit that survives power cuts and bad images. Every node runs this on its own. Next, we want the nodes to find each other and spread updates without a central host.

## Slide 19
References
[1]
MCUboot Project, "MCUboot: secure bootloader for 32-bit microcontrollers," project documentation. https://www.mcuboot.com/
[2]
B. Moran, H. Tschofenig, D. Brown, M. Meriac, "A Firmware Update Architecture for Internet of Things," RFC 9019, IETF, 2021.
[3]
ISO, "Road vehicles – Unified diagnostic services (UDS)," ISO 14229, 2020.
[4]
ISO, "Road vehicles – Diagnostic communication over CAN (DoCAN) – Part 2: Transport protocol and network layer services," ISO 15765-2, 2016.
[5]
ISO, "Road vehicles – Controller area network (CAN) – Part 1: Data link layer and physical signalling," ISO 11898-1, 2015.
[6]
CENELEC, "Railway applications – Software for railway control and protection systems," EN 50128, 2011.
[7]
CENELEC, "Railway applications – Safety related electronic systems for signalling," EN 50129, 2018.
[8]
NIST, "Secure Hash Standard (SHS)," FIPS PUB 180-4, 2015.

## Slide 20
abhinavpathak@bel.co.in · manupratapshekhawat@bel.co.in · munishkhanna@bel.co.in
Notes: Thank you. Happy to take questions.